## Slide 1: SentinelLoop
Self-Healing Machines: Predictive Maintenance for a Connected Fleet (Case Study 1)
RUL with a calibrated 90% interval · a deterministic Triage Agent that raises work orders from the interval lower bound, escalates untrustworthy inputs to a human, retrains only through a gate and keeps every decision re-derivable.
Team SentinelLoop (college to be filled)
4
C-MAPSS subsets, official test protocol
3,409
audited decisions, 0 re-derivation mismatches
112
tests, including stream = batch bitwise
55.0 min
to regenerate every number with one command
Notes: Simulated NASA C-MAPSS data; no real-world cost or safety claim. Negative results are on slides 7 and 9; limitations on slide 10.

## Slide 2: The problem, in the case study's words
INGEST
fleet sensor stream
21 sensors + 3 settings
CLEAN
fill, quality flag,
regime scaling
DETECT
degradation on a
healthy baseline
PREDICT RUL
point + 90% interval
WORK ORDER
created automatically,
one per machine
HUMAN
only for exceptions
Today failures are found after breakdowns or by fixed service intervals. Ground rules: mild imbalance (failures are rare), no manual steps once data is provided, lightweight rules without an LLM, documented design.
1
Is the order right?
Uncertainty is part of the decision (interval lower bound) and the agent is scored as a maintenance policy: late orders, discarded life, escalations.
2
Can the inputs be trusted?
Quality and drift monitors feed the agent; stress tests measure silent wrong orders on corrupted data.
3
Can a decision be explained later?
Every decision stores its inputs, thresholds, rules and model version in a hash-chained log and re-derives from it.
Honest-evidence promise
Seven hypotheses were pre-registered with success criteria; three failed as registered and are reported as such (slides 7 and 9). Nothing here is claimed as first; prior work is cited on slide 10.

## Slide 3: Architecture: one command runs the whole loop
SENSOR STREAM
batch file or
cycle-by-cycle replay
CLEAN
per-unit fill + quality flag
drop list · regime scaling
(fit on train only)
FEATURES
causal rolling mean / std /
slope over 20 cycles
MODELS
health index · HGBR RUL
+ conformal 90% interval
TRIAGE AGENT
severity from the interval
lower bound; quality, drift,
width → escalate
WORK ORDER
action · due-by cycle · top
sensors · audit chain · SQLite
DRIFT MONITOR
age-matched PSI; settings
are critical columns
RETRAIN ON NEW DATA
`sentinelloop retrain`: new file
or drift alarm → challenger
PROMOTION GATE
RMSE ≤ +2% · coverage ≥ 0.85
late orders not worse
MLflow REGISTRY
SQLite backend · champion alias
reject logged with reasons
python -m sentinelloop run --subset all
End-to-end on a CPU laptop: 36–45 s per subset, no manual step; one experiments/run_all.py invocation regenerates every number in this deck in 55.0 minutes
112 tests: train-only fits, look-ahead, bitwise stream = batch on real data, the gate, the retraining flow, audit re-derivation
Six-tab Streamlit dashboard (fleet, engine, work orders, model & monitoring, experiments, audit) reads only stored artefacts
Stream mode: the same cleaning, feature and agent code, one row at a time, with a window quality monitor; identical decisions to batch for the same cycles
36–45 s
per subset, end to end
55.0 min
run_all.py, every artefact
112
tests pass

## Slide 4: Data engineering: train-only fits, honest validation
Train-only fits: constant-sensor drop list (4–6 sensors per subset), KMeans operating regimes (6 on FD002/FD004, purity 1.00), per-regime scaling
Causal rolling mean / std / slope over 20 cycles; batch and stream use the same numpy arithmetic, so a tree model never sees a 1e-12 difference between them
Missing values: per-unit fill with a quality flag the agent reads; noise handled by the rolling features (EMA tested: −1.4 RMSE on FD001 but +6.7 on FD004, so off)
Every metrics.json and MLflow run carries the data SHA-256 hashes and the config hash
Leakage audit: the 'last cycle of a held-out training engine' protocol reports RMSE 2.5–6.9; the honest random-truncation protocol 12.4–16.6 (2.3–6.6×)
Ablation (E7): rolling features worth 2.7 RMSE on FD001; regime normalisation worth 1.1 RMSE on FD004
Chart: Validation RMSE: leakage-prone vs honest protocol
| FD001 | FD002 | FD003 | FD004
leakage-prone protocol | 2.53 | 3.49 | 2.98 | 6.87
honest protocol | 16.63 | 15.71 | 12.4 | 15.59
Why it matters
A naive validation would have claimed an error four to seven times smaller than the official test shows. We report the honest number, and both RMSEs: against RUL capped at 125 and against raw truth.

## Slide 5: Models and performance on all four subsets
Subset | RMSE capped / raw | agent's model | PHM08 | coverage capped / raw | width | naive | RandomForest
FD001 | 14.17 / 15.37 | 14.75 | 328 | 0.94 / 0.87 | 64.2 | 41.9 | 14.55
FD002 | 14.92 / 26.99 | 15.23 | 1028 | 0.89 / 0.67 | 66.4 | 44.9 | 15.17
FD003 | 13.57 / 15.32 | 13.54 | 356 | 0.92 / 0.81 | 71.6 | 43.7 | 15.22
FD004 | 15.15 / 26.89 | 15.41 | 1140 | 0.85 / 0.58 | 54.4 | 45.6 | 16.23
Chart: Test RMSE vs RUL capped at 125 (naive mean: 42–46)
| FD001 | FD002 | FD003 | FD004
RandomForest | 14.55 | 15.17 | 15.22 | 16.23
HistGradientBoosting | 14.17 | 14.92 | 13.57 | 15.15
Why HistGradientBoosting + conformalized quantile regression: CPU, seconds, retrains live, explainable; the interval is calibrated on held-out engines with random truncations (Romano et al. 2019; CQR on C-MAPSS as in Robinson 2026)
Coverage is measured per subset and stated as marginal: FD004 is below nominal (0.85) and reported as such; an asymmetric CQR option raises it to 0.89 on the ablation split for +2.4 cycles of width
Published deep models reach ≈ 11–13 RMSE on FD001 under their own protocols (prior-art document); the loop around the model is where the measured value is
Health index on real degradation (official test engines): flags 0.30–0.69 of engines within 25 cycles of failure and 0.01–0.06 of engines with more than 50 cycles left
The headline RMSE is the all-engine model; the agent acts on the 70%-engine model whose other 30% calibrate the interval (second column); both are reported
Reading the table
RMSE against raw truth is larger on FD002/FD004 because raw RUL exceeds the 125 cap early in life; the PHM08 score penalises late predictions more than early ones (convention printed in every metrics.json).

## Slide 6: Triage Agent: deterministic rules, actionable orders
Condition (L = 90% interval lower bound) | Severity | Action
L ≤ 10 cycles | CRITICAL | stop & repair, maintenance order
L ≤ 25 | HIGH | maintenance order
L ≤ 50 | MEDIUM | plan maintenance
sustained anomaly, RUL healthy | WATCH | monitor
interval wider than its calibrated limit; > 10% imputed inputs; a setting out of range; fleet drift on HIGH/CRITICAL; anomaly vs RUL conflict | ESCALATE | INSPECTION order for a human
One open order per machine; a higher severity upgrades it and pulls the due-by cycle earlier; the order carries action, RUL interval, due-by cycle, the top deviating sensors, the reasons and the model version
Every decision stores inputs, thresholds, rules fired and model version in a hash-chained audit log (slide 9)
Mild imbalance: the anomaly baseline is healthy behaviour; thresholds are set on validation engines, never on test
Decisions vs truth, official test engines
0.0%–8.0%
engines within 25 cycles of failure NOT marked HIGH/CRITICAL (per subset)
0–1
confident orders on engines with more than 50 cycles left (count per subset)
8%–19%
escalation share on clean test data
205
work-order records in the evidence run (batch + stream replay)
What this shows
Serious engines are almost all caught; the lower bound is optimistic for 5%–15% of engines, mostly early in life where it does not trigger an order.

## Slide 7: The agent as a maintenance policy: a measured trade-off
Chart: Good cycles given up per engine at the generic threshold (E1 replay)
| FD001 | FD002 | FD003 | FD004
point estimate ≤ 25 | 25.2 | 26.5 | 25.7 | 25.7
interval lower bound ≤ 25 | 40.3 | 39.2 | 36.7 | 38.9
In maintenance terms
A late order: the engine reaches end of life before the order is acted on. Discarded life: good cycles given up by ordering early. At the generic 25-cycle threshold neither policy is late on three of four subsets, so the interval's safety margin is paid for in discarded life.
Replay of complete out-of-fold trajectories: the lower-bound policy discards 11.0–15.0 more cycles per engine than the point policy at the generic threshold; late rate 0 for both on 3 of 4 subsets (H1 NOT SUPPORTED as pre-registered)
Frontier at matched late-rate targets: the interval family is better on both metrics at 3/16 points, dominated at 3/16, a trade-off elsewhere
Tuned lower-bound thresholds are unstable: seeds 42/43/44 give 6/2/0 cycles and evaluation late rates of 1%/20%/54%; a fleet must tune on far more engines
Cost sweep (assumed failure cost 25–500 cycles of life): the cost-tuned point threshold moves from 8–13 to 10–17 cycles; no money saving is claimed
E2: width-based abstention alone does not concentrate errors (acted-upon engines have equal or higher error rates on 3 of 4 subsets; escalation share 7%–15%) — H2 NOT SUPPORTED
E5: RMSE orders our point models within one to two cycles of discarded life and cannot see the policy at all — the same model acted on through its lower bound has the same RMSE and 11–15 cycles more discarded life
Related work: Mitici et al. 2023 and Lee & Mitici 2023 (decision-level metrics); the IntelliTwin repository (policy replay)

## Slide 8: Stress tests: when the inputs cannot be trusted
Fault (half of the test engines corrupted) | FD001 detection | FD002 detection | FD003 detection | FD004 detection | point agent silent wrong | full agent
20% missing values | 100% | 100% | 100% | 100% | 0%–4% | 0%
3σ noise | 98% | 100% | 100% | 100% | 1%–20% | 0%
regime shift | 100% | 100% | 100% | 100% | 0%–8% | 0%
+2σ bias, one sensor | 12% | 88% | 4% | 96% | 3%–10% | 0%
+3σ bias, one sensor | 20% | 90% | 6% | 96% | 3%–10% | 0%
Detection and false alarms are change-relative to the clean run of the same engines; zero additional per-engine false alarms in every scenario
Missing values, noise and a regime shift are caught on 98–100% of corrupted engines; a single biased sensor is a detection floor on the single-regime subsets (4–20%) and is caught on FD002/FD004 (88–96%) and at fleet level
Silent wrong orders (a HIGH/CRITICAL order issued without escalation that the clean data would not have produced): point-threshold agent 0%–20%; full agent 0% in all 20 scenarios; without the fleet-level rule 0%–12%
The cost of the fleet rule: while a fleet alarm is active, 25%–36% of the CLEAN engines are escalated to a human (clean run: 6%–18%)
One fleet-level false alarm: FD003's 50 clean engines trip the severe single-feature rule on their early-life rows (reported; the pooled 100 engines do not)
What the human sees
An INSPECTION order instead of a confident maintenance order: the reasons (data quality, insufficient evidence, drift active, conflicting evidence), the imputed fraction, the out-of-range settings and the top deviating sensors.
0%
silent wrong orders, full agent, 20 scenarios
0%–12%
without the fleet rule (per-engine evidence alone)
Honest reading
The zero is mostly the fleet rule; per-engine evidence alone is not enough, and the rule costs healthy engines. Both numbers are shown.

## Slide 9: MLOps in action: drift, gated retraining, registry, audit
Challenger trained on champion data + | FD001 | FD002 | FD003 | FD004
more data | REJECT (picp) | PROMOTE | PROMOTE | PROMOTE
+3σ sensor offset | REJECT (rmse) | REJECT (rmse) | PROMOTE | PROMOTE
labels 40 cycles too optimistic | REJECT (rmse) | REJECT (rmse) | REJECT (rmse) | REJECT (rmse)
Gate: validation RMSE ≤ champion + 2% · coverage ≥ 0.85 · late-order rate at the CRITICAL threshold ≤ champion + 0.02. Secondary run (post hoc, 20 validation rows per engine); the pre-registered run gave 4/8 outcomes as expected and is reported with it.
Label-corrupted challengers are rejected on all four subsets (RMSE 2.9–5.2 worse than the champion); the late-rate gate fires on FD003 and FD004
Honest caveats: a harmless sensor offset is promoted on two subsets because it does not hurt validation metrics; the absolute coverage floor rejected FD001's better challenger twice (fix: a floor relative to the champion)
Drift trigger (age-matched PSI): 0 false alarms in 20 clean windows on every subset; alarms on a regime shift and a sensor bias on every subset
The retraining flow is a command: python -m sentinelloop retrain --subset FD003 --new-data <file> (or --simulate-new-data, --only-if-drift); live in the demo
MLflow (SQLite backend): params, metrics, data hash, post-agent metrics, registered models with a champion alias; every scenario hands the alias back to the champion
Auditability (E6)
3,409
decisions re-derived from their records
0
re-derivation mismatches
4 / 4
logs where an in-place tamper is detected
205
orders carrying model version and severity
Not covered
The chain detects edits and reordering, not truncation of the tail or a full re-hash by someone with write access; the terminal hash is anchored in metrics.json and the MLflow run of the same pipeline run.

## Slide 10: Limitations, reproducibility, deployment
Known limitations (37 in docs/KNOWN_LIMITATIONS.md)
Simulated data; no CMMS integration; no cost saving claimed (cost ratios are swept assumptions)
The official test set was used for three design toggles and FD001's monitoring rules; FD002–FD004 are confirmatory
Single seed except the E1 seed check; tuned lower-bound thresholds unstable across seeds
Coverage subset-dependent (FD004 0.85); the absolute coverage gate floor is the weak rule
The audit chain has no external anchor beyond MLflow; thresholds must be tuned per fleet
What deployment would take
A data contract: 26 columns per cycle per machine, batch or stream
Per-fleet threshold calibration on historical run-to-failure data, validated on held-out machines
A CMMS connector for the work-order record (action, due-by, reasons, sensors)
A retraining calendar driven by the drift monitor, with the gate's reject log reviewed by an engineer
An operator sign-off on the acceptable escalation share
Reproducibility
Pinned environment (requirements.lock.txt), seeds in config, data checksums verified by 'python -m sentinelloop doctor'; experiments/run_all.py regenerates every artefact in 55.0 minutes; experiments/numbers_digest.py prints every number in this deck; 112 tests. Annex: clean-clone commands, recorded run, repository.
References: Saxena et al. 2008 (C-MAPSS, PHM08) · Romano, Patterson, Candès 2019 (Conformalized Quantile Regression) · Robinson, IJPHM 2026 (CQR for RUL on C-MAPSS) · Mitici et al. 2023; Lee & Mitici 2023 (decision-level evaluation of prognostics) · Kamariotis et al. 2024 (decision-oriented metrics) · IntelliTwin (policy replay on C-MAPSS, GitHub). Nothing here is claimed as first; the strongest wording we use is 'not found in our search'.